## Slide 1
Better Energy Better World
Efficiency | Parameter Max Efficiency | GT-EST06KH >98 2% | GT-EST08KH >98 2% |  | GT-EST10KH >98 2%
PV Input | Max. PV input power(W) Max. PV input voltage(V) MPPT Operation Voltage Range (V) Number of MPPT/PV Strings Max. PV input current(A) Short-circuit current of PV input(A) | 7800 1000 180-950 2/1 15/15 18/18 | 10400 1000 180-950 2/1 15/15 18/18 |  | 13000 1000 180-950 2/1 15/15 18/18
Battery | Max Input/Output Voltage(V) Operating Voltage Range(V) Max Charge/Discharge Current(A) Max Input/Output Power(W) Battery Type | 550 180-550 25/30 6000/6000 | 550 180-550 25/30 8000/8000 Li-ion/Lead-acid |  | 550 180-550 25/30 10000/10000
AC Input and Output | Rated Power(W) Max. Apparent AC Power(VA) Nominal AC Voltage(Vac) AC Power Frequency ( Hz) Max. AC Output Current(A) Power Factor Range OutputTHDi(@Nominal Output) | 6000 6000 380,3L/N/PE 50/60 10 |  | 10000 10000 380,3L/N/PE 50/60 15 to 0.8 lagging) <3% | 
 |  | ~1 (Adjustable <3% |  |  | 
Genaral Data | Operating Temperature Range Topology Cooling Method Ingress Protection Rating Relative Humidity DC Connection Type AC Connection Type Display Communication With Portal Communication With BMS Communication With Meter | -25C …+60C(>45C derating) Transformerless Natural convection IP65 0-100%, no condensation MC/Amphenol/Phoenix Plug-in Connector LCD RS485 (WiFi/GPRS Optinal) CAN RS485 |  |  | 
Certification | Safety EMC On-Grid standard | IEC62109-1/-2 EN61000-6-1/-2/-3,IEC61000 AS4777.2:2020 ，NRS097-2-1:2017 ，PN-EN50549-1:2019, VDE-AR-N 4105:2018,EN50549-1:2019+AC:2019-4 |  |  | 
Part Number Energy storage Nominal Voltage Maximum Charge Voltage Discharge Cut-off Voltage ESR/AC @1KHz 50% SOC Max. Continuous Charge Current Max. Continuous Discharge Current Round Trip Efficiency Charge Temperature Discharge Temperature Self-discharge Rate Recommended Depth of Discharge Maximum Depth of Discharge Cooling Method Mounting Options Shell Material Communication Monitoring Data Compliance Information Certificate Options | GTEM-400V14.4K-W 14.4kWh 400V/DC 453V/DC 292V/DC <150mΩ 50A 50A 96% 0C~+55C -20C~+60C 2% per month ≤90% 100% Natural Wall/floor Metal & ABS plastic CANbus | GTEF-345V10K-W 10.3kWh 345.6V/DC 390V/DC 300V/DC <100mΩ 15A 30A 97.7% 0C~+45C -30C~+60C 2% per month ≤90% 100% Natural Wall/floor Metal & ABS plastic CAN,RS485
 | System voltage,current,temperature,SOC,SOH,cycle,cell’s voltage IEC62619:2017,IEC62040, EN 62133:2013, EN 55032:2015+AC:2016, EN 55035:2017,EN 61000-3-2:2014, EN 61000-3-3:2013, RoHS, UN38.3, MSDS | 
System -All-in-One
Solar Panel + Inverter + BESS
Clean Power Supply
100% TESTING
Mob/WhatsApp: +86 158 0076 5605 Tel: (021) 5031 0528
E-mail: info@enerbond.com
8000
8000
380,3L/N/PE
50/60
12
from 0.8 leading
<3%
Capwall 400V14.4kWh/345V10kWh
Battery energy storage system
Inverters 6kW-8kW-10kW
WhatsApp

## Slide 2
PV1 PV2 Battery | MPPT1 DC EMI AC Breaker L L N N Battery Load Breaker DC EMI Load
Module type Power output Power output tolerances Module efficiency Voltage at Pmax Current at Pmax Open-circuit voltage Short-circuit voltage | Pmax △Pmax ηm Vmpp Impp Vac Isc | W W % V A V A | 390 | YLxxxDF54e/2(xxx=Pmax) 395 400 405 |  |  |  | 410 | 415
 |  |  | 19.97 30.27 12.89 36.80 13.68 | 20.23 30.42 12.99 36.90 13.77 | 20.48 30.56 13.09 37.00 13.86 | 0/+5 20.74 30.71 13.19 37.10 13.95 | 21.00 30.86 13.29 37.20 14.04 |  | 21.25 31.00 13.39 37.30 14.13
Power output Voltage at Pmax Current at Pmax Open-circuit voltage Short-circuit voltage | Pmax Vmpp Impp Voc Isc | % V A V A | 426.86 30.27 14.10 36.80 14.97 | 432.33 30.42 14.21 36.90 15.07 | 437.80 30.56 14.33 37.00 15.17 | 443.27 30.71 14.43 37.10 15.27 | 448.75 30.86 14.54 37.20 15.37 | 454.22 31.00 14.65 37.30 15.47
Power output Voltage at Pmax Current at Pmax Open-circuit voltage Short-circuit voltage | ηm Vmpp Impp Voc Isc | % V A V A | 296.85 28.87 10.28 34.98 11.02 | 300.63 29.01 10.36 35.08 11.09 | 304.34 29.01 10.44 35.17 11.17 | 308.17 29.14 10.52 35.27 11.24 | 312.03 29.43 10.60 35.36 11.31 | 315.80 29.56 10.68 35.46 11.38
Nominal operating cell temperature Temperature coefficient of Pmax Temperature coefficient of Voc Temperature coefficient of Isc | NOCT γ β α | C %/C %/C %/C | 39±2 -0.35 -0.28 0.05
DC
BUS
It can meet the customer's requirement of high voltage energy storage,more stable and safety.
Model: AEN-02( High voltage)
*NOCT:open-circuit module operation temperature at 800W.m-2 irradiance,20C ambient temperature,1m*s- 1 wind speed.
AEN-02 Speciﬁcations
*STC:1000W.m-2 irradiance,25C cell temperature,AM 1.5 spectrum according to EN 608904-3
Plug and play,30 mins quick installation
Electrical parameters at Nominal Operating Cell Temperature(NOCT*)
Bifacial electrical parameters at Standard Test Conditions(STC*)
Support power internet applications
Routes Diagram
Electrical parameters at Standard Test Conditions(STC*)
*Bifaciality coefficient is 70% ±5% ，rear irradiance is 135W.m-2
*Bifaciality coefficient is 70% ±5% ，rear irradiance is 135W.m-2
Solar Panel 390-415W
Intercon
-nection
Safety
Simple
Inverter
Circuit
THERMAL CHARACTERISTICS
Capwall
DC
Switch
AC
Relay
meter or CT
AC
Filter
Cloud Platform
TV
AC Input
AC SPD
DC SPD
Breaker
MPPT2
DC/DC
Load
Grid
AC
AC
AC
DC
PV
N
L