## Slide 1
DFM analysis / AS BASE PLATE EE CARRIER with 1 cavity.

## Slide 2
Customer Name:` | OECO
客户编码： | 
New Century Mould No: | NC211210
新世纪模号 | 
Customer mould No.: | Please provide
客户模号： | 
Part Name: | AS BASE PLATE EE CARRIER
产品名称： | 
Parting No: | 0000465951
产品编号： | 
Project name.: | Lamborghini
项目名称： | 
Drawing Rev./Date: | 21/12/2021
图纸编号版本/日期： | 
Part size : | 102.171 * 45.675 * 18.750 mm
产品尺寸： | 
Part weight: | 662g
产品重量： | 
Shrinkage : | Please provide
产品缩水率： | 
Cavities : | 1
模腔数： | 
Plastic Material : | PA66-GF30
Resin date sheet : | Please provide the material data sheet
胶料特性： | 

## Slide 3
O
Mould standard.: | EQV HASCO | Brand of Hot runner | YUDO
设计标准: |  | 热流道品牌 | 
Mold Type (Inch/mm): | MM | Hot runner plug type | /
模具类型 : |  | 热流道接线盒： | 
Eject leader pin and bush standard | EQV HASCO | Gate type | One valve gate on the part directly
中托司和导柱标准： |  | 流道/入胶类型： | 
Steel for core and cavity : | CAVITY:1.2738H (HRC 30~35) CORE:1.2738 (HRC28~32) | Name plate standard | N/A
模仁材料： |  | 模具铭牌标准： | 
Tie Bar Distance: | 710/630 | Water fitting type | HASCO
啤机型号: |  | 水咀标准 | 
Locating Ring(Ф): | 160 | Brand of hydraulic | N/A
法兰直径： |  | 油缸品牌 | 
Nozzle radius : | R10 | Limit s witch | N/A
炮咀R角： |  | 行程开关型号 | 
K.O thread size : | Capling type HASCO | Other standard | N/A
K.O牙: |  | 其它标准 | 
模具信息 / mold Information

## Slide 4
Parting line
PL
Cavity
Core
Parting line of injection and ejection sides. Please confirm?
VALMET – AVL - -> 23.12.2021 – CONFIRM
2022/01/11 AVL Feedback AP: OK (please check slide 6 as suggestion)

## Slide 5
Slider 1
Slider 2
Slider 3
Slider 4
Slider 2
Slider 3
Slider 4
Parting line
VALMET – AVL - -> 23.12.2021 – CONFIRM
2022/01/11 AVL Feedback AP: OK (please check slide 6 as suggestion)
Slider number 1 and 2 corrected
Slider layout, the red line are slider parting line . Please confirm?
Slider 1

## Slide 6
Slider 2
Core
2022/01/11 AVL Feedback AP: simplified design for slider 3? (initial design idea, just as suggestion/explanation. Tool design up to ELVEZ/sub-supplier)

## Slide 7
Parting line
Cavity insert layout, the red line are cavity insert parting line . Please confirm?
VALMET – AVL - -> 23.12.2021 – CONFIRM
2022/01/11 AVL Feedback AP: OK

## Slide 8
Parting line
Core insert layout, the red line are core insert parting line . Please confirm?
VALMET – AVL - -> 23.12.2021 – CONFIRM
2022/01/11 AVL Feedback AP: OK

## Slide 9
Gating
YUDO with 1 valve gate on the middle of part directly. Please confirm.
VALMET – AVL - -> 23.12.2021 – CONFIRM
2022/01/11 AVL Feedback AP: NO protrusion of gate permitted on other side of gate

## Slide 10
Ejection
Ejection layout, please confirm?
Ø10 Round Ejector Pin
Ø8 Round Ejector Pin
Ø6 Round Ejector Pin
VALMET – AVL - -> 23.12.2021 – CONFIRM
2022/01/11 AVL Feedback AP: Ejector layout confirmed

## Slide 11
Thickness Analysis
There are may some sink marks on red areas, please confirm.
VALMET – AVL - -> 23.12.2021 – CONFIRM
2022/01/10 AVL Feedback AP: Sink Marks non-critical and confirmed

## Slide 12
Part issue
There is only 0.08mm, can we remove it? Right? If ok, could you give me the modified part model.
VALMET – AVL - -> 23.12.2021 – check the 3D model for confirmation – give reply
2022/01/11 AVL Feedback AP: wall to be removed

## Slide 13
Draft Angle Analysis
There is not draft angle on green surface, we propose to add 1 degree draft angle with reducing material. Is that OK? If ok, could you give me the modified part model.
23.12.2021- Toolmaker please provide 3D model with your proposal.
2022/01/11 AVL Feedback AP: next slide
2022/01/11 AVL Feedback AP: should be covered in Slider 4?

## Slide 14
2022/01/11 AVL Feedback AP: 1.) Draft angle of 0° for surfaces with SPIROL insert mandatory according to SPIROL data sheet
2.) Missing draft angle in orange marked areas can be implemented

## Slide 15
Draft Angle Analysis
A
A
箭头所指红色面为插穿面,现为直身面,建议如上图阴影所示减胶拔模3度,减胶0.15mm，请确认？
Section A-A
This red surface is shut off, it must be 3 degree draft angle for demoulding.
So we propose to add 3 draft angle with reducing material 0.15MM. Is that OK? If ok, could you give me the modified part model.
23.12.2021- Toolmaker please provide 3D model with your proposal.
2022/01/11 AVL Feedback AP: next slide

## Slide 16
2022/01/11 AVL Feedback AP:
1.)please confirm the marked edge: if so, OK
2.) Model error detected, to be fixed for cavity to deform properly

## Slide 17
A
A
This rib only 0.5mm, there will be a filling problem. Propose to add the material from 0.5mm to 1mm. Is that OK? If ok, could you give me the modified part model.
Section A-A
This red surface is shut off, it must be 3 degree draft angle for demoulding.
Now only 0.5 degree draft angle, So we propose to add 3 draft angle with reducing material . Is that OK? If ok, could you give me the modified part model.
23.12.2021- Toolmaker please provide 3D model with your proposal.
Draft Angle Analysis
2022/01/11 AVL Feedback AP: next slide

## Slide 18
2022/01/11 AVL Feedback AP:
1.) reduce 1,5 mm to 1 mm, increase 0,5 mm to 1 mm
2.) 3° draft OK

## Slide 19
Draft Angle Analysis
红色面为插穿面,对应产品面只有1度拔模,建议拔模角度加大到3度,请确认？
VALMET – AVL - -> 23.12.2021 – CONFIRM
2022/01/11 AVL Feedback AP:
1.) Draft of 1,5° (3° in total) OK, IF dovel pin DIN 7 dia5 m6 (+0,012/+0,004) always fits Please keep indicated area at 0°

## Slide 20
Tool layout
TOP OF MOLD
Notes: cavity cutting from A&B plate directly ( without inserts), please confirm.
550mm
650mm
550mm
2022/01/11 AVL Feedback AP: Please explain during next meeting

## Slide 21
Finish requirement
Are all surfaces to be technical polished? 23.12.2021- YES.
2022/01/10 AVL Feedback EG: technical polish only required for 0° draft surfaces to minimize scratches during ejection
Proposal: SPI C3  please let us know if that is sensible

## Slide 22
Engravings
Please check the engravings layout?
2022/01/11 AVL Feedback EG: Content and priority (if there is not enough space on the part to include all six points) acc. VW10500 as follows (1=highest priority):
Logo as per VW10514 – H or Y (whichever fits the component better)
Country of origin as per VW10550
Manufacturers Code as per VW10540-1,VE10540-7
AVL Part Number + Revision Format “0000XXXXXX/XXX” (Revision to be an Insert in the tool for easy exchange)
Date Marking as per VW 10560
Material Code as per VDA260 (Plastics > 100g and Elastomers >200g required the Marking acc. VDA260 independently of this priority)

## Slide 23
Customer’s requirements
Notes:
A1, Use robot to take part out, please confirm.
A2, please provide the information if need tool label.
A3, please provide the machine data sheet and material data sheet.

## Slide 24
Thank you for your time!