## Slide 1
Production Equipment

## Slide 2
Advanced Equipment
Dry Kiln:
Large steam drying, can dry thousands of cubic meters of wood at a time, so that the wood has sufficient health time after drying, and is equipped with a wood sterilization system to protect against insects. Wood equilibrium moisture content is affected by atmospheric moisture, which varies from different region, about 11% in the north and 13% in the south China. According to different regional orders, more effective moisture content control is carried out.

## Slide 3
Wood Carbonizer：
The equipment is mainly used for the carbonization of log materials, this process effectively reduce cracking, shrinkage, and deformation. However, due to the wood structure, some materials are prone to bursting and are difficult to carbonize. They are generally dry and non-carbonized, such as cherry, oak, and sapele.
Advanced Equipment

## Slide 4
Membrane Press：
The double-sided membrane press which imported from Italy is the soul equipment of the solid wood moulding door workshop. It costs more than 220 thousand US dollars, and it can complete the double-sided large-area and large-drop shaped veneer within 4 minutes, which makes the door high stability without deformation.
Advanced Equipment

## Slide 5
Wire Drawing Machine：
This equipment is the upgrade product for the manual type, mainly used for semi-open paint products. It can enlarge the pore of the product, makes it texture clearer, paint effect more even and better, save more time, which can realize batch processing. Equipped with dust removal system, greatly improve the operating environment.
Advanced Equipment

## Slide 6
Auto Reversal Edge-sealed Production Line:
It is mainly used for the workpiece to be automatically moved to the conveying and turning after being edge-sealed. Whether the workpiece is longitudinal or horizontal, it can be automatically rotated to the feeding end.
Advanced Equipment

## Slide 7
Electrostatic Spray Coating Renovation：
① High efficiency.
② High painting rate, less waste, costs only 50% of the previous air spray gun.
③ Environmentally friendly.
④ The paint surface is more even.
Advanced Equipment

## Slide 8
LED-UV Primer Roller Painting Line：
After the upgrade, power loss is 80 KHW less than the previous mercury lamp, which avoids the pollution of the mercury lamp, ozone free, improves the production environment, greatly reduces the rework rate, makes the product more stable, does not affect the original design, and the instant drying low temperature which can meet more coating effect, saving two-thirds of the paint amount. The comprehensive production capacity is tripled, greatly reduces the cost, saving energy, greener and more efficient.
Advanced Equipment

## Slide 9
LED-UV Reciprocating Spraying Line：
Infrared induction spray, injection stops after the product is delivered.Compared with the traditional injection, saves two-thirds of the paint, while reducing the power consumption by 50 KWH, paint can be recycled. Compared with the roller painting line, it can spray shaped products. After the LED-UV reciprocating spraying machine, the grinding efficiency is higher, thus achieves quick drying, environmentally friendly and energy saving.
Advanced Equipment